## Slide 1: ESRF User Meeting 2026 PyFAI tutorial
Jérôme Kieffer
Edgar Gutiérrez Fernández
02/02/2026

## Slide 2: PyFAI tutorial - overview
02/02/2026 / 14:00 – 16:30
Each user should use its own computer (Windows, Linuc, MacOS)
1st half: concepts of pyFAI
  Motivations
  Applications
  Working philosophy
Coffee break (~15 minutes)
2nd half: hands-on
  Installation of python: venv/conda/visa
  Installation of pyFAI
  Calibration GUI
  AzimuthalIntegratrion
  Other pyFAI applications: integrate, diffmap-view, worker…

## Slide 3: PyFAI = Python Fast Azimuthal Integrator
Data collection
Setup experiment
*BM28
Data reduction
Data analysis

## Slide 4: PyFAI = Python Fast Azimuthal Integrator
Data collection
Setup experiment
*BM28
Data reduction
Calibration
3D geometry
Diffraction mapping

## Slide 5: X-ray scattering techniques
Scattering is the deflection of photons upon interaction with matter.
Source: Wikipedia
CC-BY-SA: Jeff Dahl
X ray
Monochromatic
2D camera
Sample
Bragg spots: diffraction from single crystal
Debye-Scherrer ring: diffraction from polycrystals
Monochromatic beam
Δλ≈0
2-Dimensional detectors
Shape = (x,y)
Elastic scattering
Einc = Escat
ΔE=0

## Slide 6: X-ray scattering techniques: diffraction / scattering
If the material is crystalline, the scattered photons create constructive interferences, like water waves.
Constructive interference between scattered X-ray takes place if Bragg relation is fulfilled:
If the material is disordered, the scattered photons create broad distributions of intensity.
More ambiguous and hard to analyze. Usually requires complementary techniques.
https://biosaxs.com/technique.html

## Slide 7: X-ray scattering techniques: diffraction / scattering
The study of highly crystalline materials (metals, ceramics, oxides…) is named ‘diffraction’’.
Powder Diffraction: isotropic
  Phase identification
  Crystallinity
  Lattice parameters
  Thermal expansion
  Phase transition
  Strain/crystallite size
The study of largely/inherently disordered materials (polymers, proteins, colloids…) is named ‘scattering’’.
Wide-Angle X-ray Scattering (WAXS): analog to diffraction:
  Phase identification
  Crystalllinity/orientation
Small-Angle X-ray Scattering (SAXS): micro/nano scale prove:
  Particle shape/surface
  Proteins domains
  Protein folding
  Colloid parameters
  Fiber orientation

## Slide 8: X-ray scattering techniques: diffraction / scattering
The study of highly crystalline materials (metals, ceramics, oxides…) is named ‘diffraction’’.
Powder Diffraction: isotropic
The study of largely/inherently disordered materials (polymers, proteins, colloids…) is named ‘scattering’’.
WAXS: analog to diffraction.
SAXS: micro/nano scale prove.
Both rely on the same transformation: 2D image to azimuthal average.
PyFAI is the first tool to be used after data acquisition.

## Slide 9: PyFAI: core concepts
Detector
detector_factory
Generic detector
Image / Frame / Pattern
Numpy 2D array
To be read using FabIO,
silx, h5py…
Geometry
X-ray wavelength
Position and rotations
of the detector
Integrator
Takes the detector and geometry
Takes the image
Performs the integration

## Slide 10: PyFAI: core concepts
Detector
detector_factory
Generic detector
Image / Frame / Pattern
Numpy 2D array
To be read using FabIO,
silx, h5py…
Geometry
X-ray wavelength
Position and rotations
of the detector
Integrator
Takes the detector and geometry
Takes the image
Performs the integration

## Slide 11: PyFAI: core concepts
Detector
detector_factory
Generic detector
Image / Frame / Pattern
Numpy 2D array
To be read using FabIO,
silx, h5py…
Geometry
X-ray wavelength
Position and rotations
of the detector
Integrator
Takes the detector and geometry
Takes the image
Performs the integration

## Slide 12: PyFAI: core concepts
Detector
detector_factory
Generic detector
Image / Frame / Pattern
Numpy 2D array
To be read using FabIO,
silx, h5py…
Geometry
X-ray wavelength
Position and rotations
of the detector
Integrator
Takes the detector and geometry
Takes the image
Performs the integration

## Slide 13: PyFAI: core concepts
Detector
detector_factory
Generic detector
Image / Frame / Pattern
Numpy 2D array
To be read using FabIO,
silx, h5py…
Geometry
X-ray wavelength
Position and rotations
of the detector
Integrator
Takes the detector and geometry
Takes the image
Performs the integration

## Slide 14: PyFAI: core concepts
Detector
Geometry
Integrator
RAW DATA
PROCESSED DATA

## Slide 15: Geometry instance
A geometry is fully defined by:
  A detector instance
  Sample to detector distance (in meters)
  Wavelength of the beam (in meters)
  Three rotations of the detector
  Coordinates of the point of normal incidence (PONI), from the sample to the detector plane.
Normally, the calibration of the geometry is fully done through the graphical interface.

## Slide 16: Calibration of geometry: pyFAI-calib2
Calibration is made after measuring a standard sample:
  LaB6, Cr2O3, AgBh…
Choosing the correct detector (+ orientation, binning, mask…)
Selecting the Debye-Scherrer rings associated to the standard
Fitting the rings
Refinement
Validation
Saving of .poni file
.poni file

## Slide 17: Calibration of geometry: pyFAI-calib2
Calibration is made after measuring a standard sample:
  LaB6, Cr2O3, AgBh…
Choosing the correct detector (+ orientation, binning, mask…)
Selecting the Debye-Scherrer rings associated to the standard
Fitting the rings
Refinement
Validation
Saving of .poni file
.poni file

## Slide 18: PyFAI: creating an integrator
Detector
Geometry
Integrator

## Slide 19: PyFAI: creating an integrator
Integrator

## Slide 20: PyFAI: creating an integrator
Integrator

## Slide 21: PyFAI: creating an integrator
Integrator
*FiberIntegrator is targeted to Grazing Incidence experiments

## Slide 22: PyFAI: loading data
Integrator
RAW DATA

## Slide 23: PyFAI: loading data
Importing data is made through other python packages:
  FabIO
  Silx
  h5py
Common file formats:
  .edf
  .tiff
  .h5
Visualizing is made through:
  matplotlib
  seaborn
  silx

## Slide 24: PyFAI: loading data
Integrator
RAW DATA
integrate1d

## Slide 25: PyFAI: loading data
Integrator
RAW DATA
integrate2d

## Slide 26: What happens during an integration
1) Get the coordinates of every corner of every pixel of the detector (in meters).
  3 coordinates per corner, 4 corners per pixel
  Detector of 1000x1000 = 106 pixels = 1Mpix * 4 (corners) * 3 (coordinates) * 4 (bytes) = 48 Mbytes
2) Offset the detector’s origin to the PONI and rotate around the sample.
3) Calculate the radial (2theta) and azimuthal (chi) positions of each corner.
4) Calculate normalization matrix: polarization, solid-angle, flat-field...
5) Assign each pixel to one or multiple bins.
6) Histogram bin position with associated intensities
7) Histogram bin position with associated normalizations
8) Return bin position and the ratio of sum of intensities / sum of norm.

## Slide 27: Integration algorithms
Histogram
  Pixel by pixel procedure.
  Each pixel is split over the bins it covers.
  Corner coordinates have to be calculated (4x slower initialization).
  The slow down is function of the oversampling factor, for every image.
  Serial read → Random write
Sparse Matrix Multiplication
  Bin by bin procedure.
  Creates and stores a sparse matrix with all the integration information.
  The sparse matrix can be huge: longer initialization related to the oversampling factor.
  No performance penalty on the integration itself.
  Serial write ← Random read

## Slide 28: Pixel splitting
No splitting: one pixel to one single bin upon in which bin the center of the pixel is falling.
Bin (k)
Bin (k-1)
Bin (k+1)
The intensity of each bin is the sum of the intensity of the pixels whose center falls into the radius bin

## Slide 29: Implementation
Python
Use numpy methods
No initialization
Slow, no cache
Non-recommended (not popular)
Cython
Use cython methods
No initialization
Faster than python, no cache
Recommended to integrate 10s frames
OpenCL
Use parallelization through CPU/GPU
Initialization ~1-3 s
Cache
Potentially fast, depending on the GPU
Best option for large data

## Slide 30: pyFAI interfaces
Applications:
  GUI applications: pyFAI-calib2, pyFAI-integrate, pyFAI-diffmap-view
  Batch mode: worker
  Scriptable applications: pyFAI-average, pyFAI-saxs, pyFAI-waxs, diff_tomo
Python interface:
  High level, direct API: scripts, Jupyter notebook
  Mid level: manually creation of detectors, integrators, units…
  Low level: manually setting the integrator engines
It is up to the user to choose the way he/she uses pyFAI

## Slide 31: Latest news from pyFAI
pyFAI-2025.12.1
Parallax correction API
  Absorption coefficients of detector materials
  Detector thickness
Improved module for crystallography
Grazing Incidence integration on pyFAI-integrate
Arithmetic operations of containers
GUI bugs fixed

## Slide 32: Reasons to choose pyFAI
Faster than others
  First tool using sparse matrix multiplication to perform integration
  All computation intensive kernels are ported to C, C++ or OpenCL
  PyFAI is the only azimuthal integration tool benefiting from GPU
Versatile (increasing with every version)
  Wide space to vary the integration protocol
  Generic geometry
  Most detectors already defined (+ custom detector through Nexus file)
  Graphical user interface alternatives (thanks to Valentin Valls)

## Slide 33: Acknowledgements
Main author: Jerome Kieffer
Contributors: 43
Former data analysis unit colleagues:
  Valentin Valls
  Loic Huder
  Thomas Vincent
  Claudio Ferrero
ESRF Beamlines:
  BM01, BM02, ID02, ID11, ID13, ID15a, ID15b, ID21, ID22, ID23, BM26, ID27, BM28, ID28, BM29, ID29, ID30, ID31...
Trainees:
  Aurore Deschildre
  Frederic Sulzmann
  Guillaume Bonamis
Other synchrotron/labs
  Soleil: Fred Picca
  Clemens Prescher (Dioptas)
  Sesame: Philipp Hans
  NSLS-II, ALS, APS…
International Grants:
  LinkSCEEM-2 grant:
    Dimitris Karkoulis
    Giannis Ashiotis
    Zubair Nawaz

## Slide 34: ESRF User Meeting 2026 PyFAI tutorial
Jérôme Kieffer
Edgar Gutiérrez Fernández
02/02/2026